TIMISOARA COMBINED HEAT AND POWER

FOR CET SUD LOCATION

MONITORING PLAN

SC Colterm S.A.

Episcop Joseph Lonovici, 4

Timisoara, 300092

Romania

Tel. +40 256 435726

Fax. +40 256 431616

www.colterm.ro

Project advisor:

SC ENINVEST SA

Lacul Tei Blvd., 1 - 3

Bucharest

Romania

Tel: +40 21 211 9446

Fax: +40 21 211 5892

office@eninvest.ro

JANUARY 2006

CONTENT

1.INTRODUCTION..........................................................................................................3

2.PROJECT-SPECIFIC INDICATORS.........................................................................3

3.DEFAULT VALUES....................................................................... ..............................6

4.LEAKAGE INDICATORS............................................................................................6

5.MONITORING PROCESS...........................................................................................7

5.1 COLLECTION..........................................................................................................................8

5.2 DOCUMENTATION................................................................................................................8

5.3 ARCHIVING.............................................................................................................................8

5.4 GHG EMISSION REDUCTION CALCULATION.................................................................8

5.5 VERIFICATION.......................................................................................................................8

5.6 TRAINING PROCESS.............................................................................................................9

5.7 QUALITY CONTROL PROCESS..........................................................................................9

5.8 AUTHORITY OF PROCESS..................................................................................................9

# LIST OF FIGURES

FIGURE 1: PROJECT BOUNDARY................................................................................3

# LIST OF TABLES

TABLE 1: EMISSIONS BY SOURCES..........................................................................4

TABLE 2: MONITORED DATA.....................................................................................5

Monitoring Plan								January,2006

- INTRODUCTION

Monitoring of project performance is crucial to ensure that reduction units claimed for JI project are justified. The monitoring activities should ensure that indicators that show the greenhouse gas emission level from the project are recorded in a way that enables comparison with baseline scenario. Subsequently the difference in the project and the baseline emissions can be claimed as emissions reductions. 1

The monitoring activity can only start once the project is operational, which is planned to be in the fourth quarter of 2005. It has to be carried out by determined parties. The monitoring plan describes who will carry out the monitoring activities and who has the final responsibility.

In most case, some sort of monitoring of the project performance is undertaken as part of the operation of the project, f.e. the electric output of a project will be measured and monitored for purposes of the sales of electricity. This data can be used to calculate the emission reductions attributable to the project. The linked GHG monitoring activities and existing monitoring activities, such as electricity output, will reduce the costs of monitoring activities for JI purposes.

- PROJECT-SPECIFIC INDICATORS

The definition of the project boundaries is an important issue for the development of the monitoring plan. The project boundary selected for the baseline and for monitoring are the same.

CO2 Emissions

Emissions included in the project- after project implementation

CO2 Emissions

Emissions included in the project-existing situation

Figure 1: Project boundary

1ERUPT vol.1, June 2003, page 26

Monitoring Plan							January,2006

The emissions included for the calculation are the same:

| On site emissions |
| --- |
| Project | Current situation |
| CO2 emissions from producing power for internal consumption | - |
| CO2 emissions from producing heat for the grid | CO2 emissions from producing heat for the grid |
| CO2 emissions from producing power for the grid | - |
| Off-site emissions |  |
| Project | Current situation |
| - | CO2 emissions from producing power in other power plants |
| - | CO2 emissions from transporting power for internal consumption from other power plants |
| CO2 emissions from fuel production and transport | CO2 emissions from fuel production and transport |

Table 1: Emissions by sources

To enhance the reliability of indicators used for crediting, it is recommended to use for monitoring and reporting, to the extent possible, those indicators that are already in use for normal business practice. The advantage is that parties outside the project already have verified such indicators. This enables the project developer to use established data records from their archives, instead of developing a new set of records. An example is a district heating system, which typically will have records from purchased fuel, as well as records from sold heat and/or electricity.2

Considering the project boundary, the following data need to be monitored in order to estimate project and baseline emissions, and emissions reductions:

The important project factors for controlling and reporting of the project performance are the output of heat and electricity and the fuel consumption. These factors will be measured on a regular basis during operation:

- Volume of natural gas consumed, m3

- Volume of lignite consumed, t

- Cogeneration heat supplied, GJ

- Cogeneration electricity consumed in own plant, MWh

- Cogeneration electricity supplied to NPG, MWh

2ERUPT vol. 1, June 2003, page 26

Monitoring Plan							January,2006

The table below shows the different project factors to report:

| ID number | Data type | Data variable | Data unit | Measured (m) Calculated (c) or estimated (e) | Recording frequency | Proportion of data to be monitored | How will Data be archived? (electronic/ paper) | For how long is archived data to be Kept? |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Volume of natural Gas consumed | MECNG | tm3 | m invoices and through plant meters | monthly | Electronic (spreadsheet) | 8 years | - |
| 2 | Volume of lignite consumed |  | t | m invoices and through boiler weighing machines | monthly | Electronic (spreadsheet) | 8 years | - |
| 3 | Cogeneration heat supplied | MCHO | GJ | m | monthly | Electronic (spreadsheet) | 8 years | - |
| 4 | Cogeneration electricity consumed in own plant | MCEO | MWh | m | monthly | Electronic (spreadsheet) | 8 years | - |
| 5 | Cogeneration electricity supplied to NPG | MCEO | MWh | m | monthly | Electronic (spreadsheet) | 8 years | - |

Table 2: Monitored data

From these monitored data, and emissions factors, it will be possible to determine CO2, CH4 and N2O emission in the project and baseline situation.

A certain amount of electricity will be bought from the system during the plant start-up phase. This amount of electricity will be measured and subtracted from the quantity of electricity produced.

Monitoring Plan							January,2006

- DEFAULT VALUES

In order to calculate the project emissions, some default values may be used for monitoring purposes. Typically this includes: national electricity grid carbon factors, IPCC default factors for the greenhouse gases, specific analysis of natural gas that is sustained well enough by statistics to determine them as default values, as well as industrial standards for efficiencies or other standardized values from recognized sources.3

- LEAKAGE INDICATORS

For project leakage indicators, business-linked indicators are not likely to be available for all purposes. Projects generally will be less in control of the measurement and/or monitoring of leakage effects than of variables with direct impact on project operations. The nature of the project will determine the need and possibility to estimate project leakage. Data from suppliers/utilities may be of help to monitor and report leakage effects, as well as available public statistics. Specific surveys with the aim to monitor and estimate project leakage, e.g. in energy efficiency projects, may also be required.

The indirect impacts (leakage) are related to undesirable GHG emissions occurring as a side effect of the project. As described in the baseline study, there is no expected leakage for this project. Therefore there will  not be a specific monitoring activities regarding this aspect.

3 ERUPT

Monitoring Plan							January,2006

- MONITORING PROCESS

The monitoring process consists of the following process steps:

- Collection

- Documentation

- Archiving

- GHG emissions reduction calculation

- Verification

|  | Collection | Documentation | Archiving | Emission Red. calculation | Verification |
| --- | --- | --- | --- | --- | --- |
| Frequency | monthly | monthly | monthly | every half a year | every two years |
| Responsibility | operational staff | operational staff | controlling department | controlling department | Independent entity |
| Form | excel sheet | excel sheet | excel sheet | excel sheet | verification document |
| Send to | controlling department | controlling department | Independent entity | Project participants (Municipality, Ministry of Environment and Waters Management, STEM, independent entity, Swedish Embassy Bucharest) | Project participants (Municipality,Ministry of Environment and Waters Management, STEM, independent entity, Swedish Embassy Bucharest |

Monitoring Plan							January,2006

  - Collection

- Frequency: monthly

- Responsibility: operational staff

- Method:

  - Volume of natural gas consumed: invoices checked with stock (cross check through plant meters)

  - Volume of lignite consumed: invoices checked with stock (cross check through boiler weighing machines)

  - Cogeneration heat supplied: operational statistics(cross check: invoices)

  - Cogeneration electricity consumed in own plant: operational statistics (cross check: invoices)

  - Cogeneration electricity supplied to the national power grid :operational statistics (cross check : invoices)

.   Form : excel sheet

Sent to: controlling department

5.2. Documentation

Frequency : monthly

Responsibility : controlling department

Form : excel sheet

Send to : controlling department

5.3. Archiving

Frequency : monthly

Responsibility : controlling department

Form : excel sheet

Send to : independent entity

5.4. GHG emission reduction calculation

Frequency : every half a year

Responsibility : controlling department

Form : excel sheet

Send to : project participants ( Municipality, MEWM, STEM, independent entity)

5.5. Verification

Frequency : every two years

Responsibility : independent entity

Form : verification document

Send to : project participants

5.6. Training process

The controlling department will develop and ensure training process.

5.7. Quality control process

Quality control to enable data quality and data changes.

5.8. Authority of process

Controlling department ( or Director of Operations).

# Text boxes

Heat Grid

Fuel

CET Timisoara Sud

Electricity Grid

Fuel

CET Timisoara

Electricity Grid

Other Power Plants

Other Power Plants

Heat Grid