| Approval status |  | Registration no. |  | Date |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Project reference number | 26-00-725 |
| Project name | “Bulgarian Energy Efficiency and Renewable Energy Portfolio Project” |
| Project location | Energy Efficiency (PDD-EE) Sugar Plants are located in Gorno Oriahovitsa Zebra is located in Novi Iskar Pirinplast is located in Goce Delchev Renewable Energy (PDD-RE) Trakija Gas Plovdiv region (between Bojkovo and Hrabino) Delektra Hydro Pazardjik region (near Lesitchevo) Wiwa Agrotex Alfatar City |
| Project description | The project consists of 6 portfolio projects. Two PDDs have been prepared and validated for the Portfolio of Projects. One PDD for the energy efficiency projects (three projects) and one for the renewable energy projects (three projects). 1 Sugar Plants JSC The project involves two sub projects: i. ECO 1 - reconstruction and improvement of energy efficiency of an existing coal fired steam boiler (PK-35-39 No. 3), used for steam and electricity production; ii. ECO 2 - establishment of two heat exchangers for heating, utilizing the output steam of installed new back pressure steam turbine and though increasing the quantity of the co-generated electricity. 2 Zebra AD JSC The project of Zebra JSC aims at the improvement of the energy efficiency at the rubber products production plant, through the implementation of three groups of energy savings measures: Implementation of combined steam/power production, based on gas engine, with utilization boiler, water treatment, de-aeration devices and steam pipeline replacement and installation of an electric generator; Utilization of waste heat for process and heating purposes; Replacement of the Calendar engine. 3 Pirinplast The project of Pirinplast JSC envisages the replacement of 5 low efficient injection machines with new highly efficient injection moulding machines, characterized by a high productivity and low energy consumption. Improvement of both productivity and quality of the manufactured products as well as higher efficiency will be achieved. 4 Trakija Gas: The construction of the run-of-river Small Hydro Power Plant (SHPP) Tumrush for the generation of electric energy. The SHPP Tumrush is constructed for the generation of 15,115 MWh/year depending on actual hydrological conditions in a mean-water year and installed capacity at the generator clamps of 5,140 kW. Electricity will be delivered to the Bulgarian Electricity Grid. 5 Delektra: The first unit of SHPP Lesitchevo is expected to generate 10,880 MWh in a mean-water year, with maximum generator capacity at the generators clamps of 1,527 kW. The second unit with the same capacity is expected to generate 5,580 MWh in a mean-water year. The total planed electricity production of the plant is 16,460 MWh in a mean-water year. Electricity will be delivered to the Bulgarian Electricity Grid. 6 Wiwa Agrotex: The steam station for combustion of biomass (straw) will consists of two steam boilers with a total output of 8 t/h steam. The steam will be sold to one consumer, namely the Bio-etil production plant owned by Evro- Etil Ltd in Silistra city. Plant is expected to utilise 13,317 t of straw. |
| Project developer | United Bulgarian Bank (Co-ordination of the Portfolio Project) 5 Sveta Sofia Street, 1040 Sofia Mrs. Hrisimira Malcheva (Tel +359 28112229, malcheva_h@ubb.bg) Mr. Stefan Vassilev (Tel +359 28112594,vassilev_st@ubb.bg) 1. Sugar Plants JSC Sveti Knijaz Boris 1 Str. R29, Gorna Oryahovica, Bulgaria Mr. Georgi Alexiev Yzynov (Tel +359 61841461, office@zaharnizavodi.com) 2. Zebra AD 1280 Novi Iskar, Sofia Mrs. Slavka Stefcheva (Tel +359 29360654, e-mail: zebra@mail.orbitel.bg) 3. Pirinplast AD 2900, Goce Delchev, Bulgaria Mr. Stojan Vakareev (Tel +359 75169022, pirinplast@goce.net) 4. Trakija Gas Slavijanski Blvd. R12, Stara Zagora Mr. Nasko Dimitrov Stoyanov (Tel +359 42600426, svg@sz.inetg.bg) 5. Delectra Hydro Maior Parvan Toshev Str. R26, floor 1, flat 1, Sofia Mr. Georgi Denkov (Tel +359 29582321, delectra@spnet.net) 6. Wiwa Agrotex Dobrydja Str. R 1, floor 5, P.O.Box 221, 7500 Silstra Mr. Radoslav Vilhem Shynk (Tel +359 86820634, wiwaagro@mbox.infotel.bg) |
| Project type | 3 energy efficiency projects; and 3 renewable energy projects |
| Total investment | Total investment associated with the six projects is EUR 7 million. See table below. name company project type investment (EUR) Sugar Plants EE 1,408,463 Zebra AD EE 1,311,317 Pirinplast EE 550,000 Trakija Gas RE 2,147,426 Delektra Hydro RE 1,230,429 Wiwa Agrotex RE 408,908 7,056,543 |
| Expected emission reductions | The portfolio is expected to reduce 612,126 tonne CO2e, of which 204,167 in the period 2005 – 2007 (inclusive) and 407,960 in the period 2008 – 2012 (inclusive). See overview below. |
| Project start | Sugar Plants: July 2004; Zebra AD: July 2005; Pirinplast: March 2005. Trakija Gas: August 2005 Delektra Hydro: January 2005; Wiwa Agrotex: February 2006; |
| Project duration | Operational lifetime: Sugar Plants: 8 years; Zebra: 7 years; Pirinplast: 7 years. Trakija Gas: 30 years; Delektra Hydro: 30 years; Wiwa Agrotex: 12 years; |
| Credit period | Beginning | 01-01-2005 | End | 31-12-2012 |
| Emission reduction start | 01-01-2005 |
| Buyer | European Bank for Reconstruction and Development for the account of the Netherlands |
| Contact person | Mr. Egbert Liese |
| Contact details | One Exchange Square, London EC2A 2JN, UK Tel +44 20 73387177, LieseE@ebrd.com |
| Validator | TÜV Suddeutschland |
| Contact person | Mr. Werner Betzenbichler |
| Contact details | Westendstr. 199, 80686 Munich, Germany Tel +49 8957912170, Werner.Betzenbichler@tuev-sued.de |
| Validation date | RE PDD: 03-05-2006 EE PDD: 29-09-2006 |
| Validation report Nr | RE PDD: Report No. 733 895-2, Rev. 01 EE PDD: Report No. 733 895-1 |
| PDD consultant | DHV |
| Contact person | Mr. Herman Jan Wijnants |
| Contact details | P.O. Box 1076, 3800 BB Amersfoort, the Netherlands Tel +31 334682917, Hermanjan.Wijnants@dhv.nl |
| Credit period | 2005 – 2012 |
| Information on early credits | Project |
| Information on credit sharing | All the reductions are aimed to be sold to the Netherlands-EBRD Carbon Fund |
| GHG emissions reductions by years |
| Emissions reduction Energy Efficiency and Renewable Energy Portfolio, Bulgaria [CO2eq/MWh/y] Year SugarPlants Zebra Pirinplast Tarkija Delektra Wiwa Total EE Total RE Total 2005 1,814 1,360 10,566 10,064 13,365 3,175 33,995 37,170 2006 7,543 2,064 2,332 18,123 19,066 13,365 11,940 50,554 62,494 2007 8,400 8,349 2,332 18,123 19,736 13,365 19,081 51,223 70,304 AAUs 17,757 10,413 6,025 46,811 48,866 40,095 34,195 135,772 169,968 2008 8,400 8,349 2,332 18,123 19,736 13,365 19,081 51,223 70,304 2009 8,400 8,349 2,332 18,123 19,736 13,365 19,081 51,223 70,304 2010 8,400 8,349 2,332 18,123 19,736 13,365 19,081 51,223 70,304 2011 8,400 8,349 2,332 18,123 19,736 13,365 19,081 51,223 70,304 2012 8,400 8,349 2,332 18,123 19,736 0 19,081 37,858 56,939 ERUs 41,998 41,744 11,661 90,614 98,678 53,460 95,403 242,752 338,155 TOTAL 59,755 52,157 17,686 137,426 147,544 93,554 129,599 378,524 508,123 |
| Description of technology changes, mention both new and old technology used (if any) | Technology used in all projects is based on Best Available Technology and compliant with EU regulations. |
| Emission factor per unit of production (e.g. per tonne of cement/fertilizer) | CEF Unit tCO2e CEF Electricity generation tCO2e/MWh 1.199 CEF Coal tCO2e/t 1.336 CEF heavy oil tCO2e/t 0.812 CEF Electricity Consumption tCO2e/MWh 1.3189 CEF for Natural Gas tCO2e/GJ 0.0558 |
| JI Supervisory Board approval Nr No. |  | Date |  |
| UNFCCC registration Nr |  | Date |  |
| Verification | Not selected yet |
| Contact person |  |
| Contact details |  |
| Verification date |  |
| Verification report Nr |  |
| Sold ERUs |  | Date |  |